## Slide 1: Electricity Primer
Cyber stars - 2014

## Slide 2: What is electricity?
A form of energy
  We can harness to produce heat, movement, light, etc
Three components:
  Current: Flow of electrical energy through a circuit
    Flows from positive side to negative side (Direct Current)
    Measured in Amps (A)
  Voltage: Measure of difference in potential energy between a circuit’s positive and negative ends
    Measured in Volts (V), the great the volts, the faster electricity moves
  Power: Measure of the rate at which a device converts energy from one form into another
    Measured in Watts (W)
    100W light bulb is brighter than a 60W bulb due to the rate at which it converts

## Slide 3: Electrical Components
Resistors: Reduces the flow of electrical current in a circuit
  Slows down and is converted to heat
  We need resistance when we have components that only need so much electricity – such as an LED
  Too much and we can kill the component
  Measured in Ohms
    From 0 to millions of Ohms of resistance

## Slide 4: Electrical Components
Light Emitting Diode
  Converts electrical current to light
  Polarized: electricity can only enter and leave in one direction
  Anode (positive side) – entry point
    Long leg
  Cathode (negative side) – exit point
  May need to use Ohm’s law…

## Slide 5: Pulse Width Modulation (PWM)
Vary how much time we have between an LED’s on/off states
  Gives the illusion of it being dimmer – it’s not, it just wasn’t lit for very long
Pins on our boards with a tilde (~)
  3, 5, 6, 9, 10, 11
Use analogWrite(pin, duty_cycle)
  Duty_cycle = value between 0 and 255

## Slide 6: Electrical Components
Transistor: can turn on/off the flow of a much larger current than the Uno can handle
  We can use to control a transistor with a digital output pin
Pins have a particular order:
  Collector: Larger current we want to switch enters here
  Base: Allows current from the collector to enter
  Emitter: Current flows out of the emitter
Can switch a small amount of current (100mA) to a much larger amount – 30 V – much more than the Arduino Uno’s digital out

## Slide 7: Electrical Components
Rectifier Diode
  Allows current to flow in ONE direction only
  Can be used to protect components in a circuit
  But, they also cause a drop in voltage